## Slide 1: Internet of Things
Module-1
Basics of IOT

## Slide 2: What is IoT?
Connect the unconnected.
Objects that are not currently joined to a computer network, namely Internet, will be connected so that they can communicate and interact with people and other objects.
IoT is a technology transition in which devices will allow us to sense and control the physical world by making objects smarter and connecting them through an intelligent network.
It allows for improvements in efficiency, accuracy, automation and the enablement of advanced applications.

## Slide 3: Genesis of IoT
Started between the years of 2008 and 2009.
More “things” connected than people in the world.
The term “Internet of Things” was created by Kelvin Ashton.
Kelvin used the phrase to explain a new idea related to linking the company’s supply chain.
Kelvin quoted “ In the twentieth century, computers were brains without senses.

## Slide 4: Evolutionary Phases of the Internet
Internet Phase | Definition
Connectivity | Connected people to email, webservices and search that information which can be easily accessed
Network Economy | Enabled with e-commerce and supply chain enhancements along with collaborative engagement to drive increased efficiency in business process
Immersive Experiences | Extended the Internet experience to encompass widespread video and social media while always being connected through mobility.
Internet of Things | Adding connectivity to objects and machines in the world around us to enable new services and experiences.

## Slide 5
Evolutionary phases becomes more value for business, government and society.
In First Phase:
Connectivity began in mid 1990.
Email and internet were considered as luxuries for companies and corporations.
Dial-up modems and basic connectivity were considered.
Connectivity and speed continued to improve, connectivity was not a major challenge.
In Second phase:
It began with Network Economy.
E-commerce and digitally connected supply chains became rage and caused disruptions.
Vendors and suppliers became closely interlined with producers and online shopping experienced incredible growth.

## Slide 6
In Third phase:
Emergence of social media, collaboration and widespread mobility on a variety of devices.
Use of multiple platforms from mobile phone, tablets , laptops and desktop.
Pervasive computing enables communication and collaboration as well as social media across multiple channels via email, texting, voice and video.
In Last Phase:
99% still things are not connected.
Machines and objects in this phase connect with other machine objects along with humans. Business and society have already started down this path and are experiencing huge increases in data and knowledge.

## Slide 7: IoT and Digitization
IoT focuses on connecting “things” such as objects and machines to a computer network.
E.g: In a shopping mall where Wi-Fi location tracking has been deployed. The “things” are Wi-Fi devices. Wi-Fi location tracking is simply the capability of knowing where a consumer is in a retail environment through his or her smart phone’s connection to the retailer’s Wi-Fi network.
Tracking real-time location of clients provides a specific business benefit to the mall and shop owners.It helps the business to understand the shoppers tend to congregate and how much time they spend in different parts of a mall.
Analysis of this data can change the product display and advertising, placing the shop, how much to charge and station security guards.

## Slide 8
Digitization is defined as the conversion of information into a digital format.
E.g. photography industry has been digitized. Everyone has digital cameras either standalone devices or built into their mobile phones. other examples such as video rental industry and transportation. People went to store to rent or purchase video tapes or DVDs of movies. With digitization, just everyone is streaming video content or purchasing movies as downloadable files.
Transportation industry is currently undergoing digitization in the area of taxi services. Businesses such as Uber and Lyfy use digital technologies to allow people to get a ride using mobile phone app. This app identifies the car, the driver and fare.
In the context of IoT, digitization brings together things data and business process to make people can relate to is in the area of home automation with popular products such as Nest. With Nest, sensors determine your desired climate settings and also tie in other smart objects such as smoke alarms, video cameras and third-party devices.

## Slide 9: IOT Impact
Today about 0.06% of things are connected to the internet today.
Cisco has predicted that by 2020, the number will reach to 50 billion.
New connections will lead to $19 trillion in profits and cost savings.
Managing and monitoring the smart objects using real-time connectivity enables a whole new level of data-driven decision making.

## Slide 10: Connected Roadways
Iot is going to enable self-driving vehicles to better interact with transportation system around them through bi-directional data exchanges while also providing important data to the riders.
self-driving vehicles need always-on, reliable communications and data from other transportation-related sensors.
Connected roadways is the term associated with driver and driverless cars by integrating with surrounding transportation infrastructure.

## Slide 11: Connected Roadways
Car is ready with the basic sensors such as oil pressure, tire pressure, temperature and other operating conditions and provide data around the core car functions.
Behind the steering wheel the driver can access the data while controlling the car using equipment such as steering wheel, pedals and so on.
Driver must be able to handle and make critical decisions while concentrating on driver safely.
Sensors are becoming IP-enabled to allow easy communication with other systems both inside and outside the car.
New sensors and communication technologies are being developed to allow vehicles, traffic signals, school zones and other elements of the transportation infrastructure.

## Slide 12: Current challenges Being addressed by connected Roadways
Challenge | Supporting Data
Safety | According to US Department of Transportation, 5.6 million crashes were reported in 2012 alone, resulting more than 33,000 fatalities. IoT and the enablement of connected vehicle technologies will empower drivers with the tools they need to anticipate potential crashes and significantly reduce the number of lives lost each year.
Mobility | Connected vehicles mobility applications can enable system operators and drivers to make more informed decisions, which can reduce travel delays. Congestion causes 5.5 billion hours of travel delay per year and reducing travel delay is more critical than ever before. Communication between mass transit, emergency response vehicles and traffic management infrastructure help optimize the routing of vehicles.
Environment | According to the American public Transport Association, each year transit systems can collectively reduce carbon dioxide (CO2) emissions by 16.2 million metric tons by reducing private vehicle miles. Connected vehicle environmental applications will give all travelers the real-time information they need to make “Green” transport choices.

## Slide 13
With IoT connected roadways, a concept known as Intersection Movement Assist(IMA) is possible.
It warns a driver response in a self-driving car. When it is not safe to enter an intersection due to a high probability of collision. Or another car has run a stop sign or strayed into wrong lane.
IMA is one of the possible solutions that emerge when we start to integrate IoT with both traditional and self-driving vehicles.
Other solutions include such as automated vehicle tracking, cargo management and road weather communications.

## Slide 14
With vehicle tracking, a vehicle’s location is used for notification of arrival times, theft prevention or highway assistance.
Cargo management provides precise positioning of cargo as it is en route so that notification alerts can be sent to a dispatcher and routes can be optimized for congestion and weather.
Road weather communications use sensors and data from satellites, roads and bridges to warn vehicles of dangerous conditions or inclement weather on the current route.
As cars continue to become more connected and capable of generating continuous data streams related to location, performance, driver behavior and much more the data generation potential of a single car is staggering.
It is estimated that a fully connected car will generate more than 25 gigabytes of data per hour. Multiply that by the number of hours a car is driven per year and number of cars on the road, the amount of data generated, transmitted and stored in the cloud will be in the zettabytes range per year.

## Slide 15
The data generated by car needs to be handled in a secure and reliable way, means the network needs to be highly available.
Automobile data is extremely useful to a wide range of interested parties. Tire companies can collect data related to use and durability of their products in a range of environments in real time. Automobile manufacturers can collect information from sensors to better understand how the cars are being driven.
Car sensors will be able to interact with third-party applications such as GPS/maps, to enable dynamic rerouting to avoid traffic, accidents and other hazards.
Internet –based entertainment, including music, movies and other streaming or downloads, can be personalized and customized to optimize a road trip.
GPS navigation systems become more integrated with sensors and wayfinding applications. E.g. if you prefer a coffee shop, through the use of a cloud-based data connector, the navigation system will be able to provide routing suggestions that have you drive your car past right to the coffee shop.

## Slide 17: Connected Factory
Main challenges facing manufacturing in a factory environment today include the following:
Accelerating new product and service introduction to meet customer and market opportunities.
Increasing plant production, quality and uptime while decreasing cost.
Migrating unplanned downtime.
Securing factories from cyber threats
Decreasing high cabling and re-cabling costs
Improving worker productivity and safety.

## Slide 18: Connected Factory
New ways to manufacture in a more cost-effective manner. Plant managers are entirely focused on gains in plant efficiency and operational agility. A convergence of factory-based operational technologies and architectures with global IT networks is starting to occur, also referred as connected factory.
Sensors are advanced which attains new level of connectivity. They gain the ability to communicate mainly using the Internet Protocol(IP) over Ethernet infrastructure.
The devices in the plant floor are becoming smarter in their ability to transmit and receive large quantities of real-time informational and diagnostic data.
Ethernet connectivity is becoming pervasive and spreading beyond just the main controllers in a factory to devices such as the robots on the plant floor.
IP-enabled devices are being added, including video cameras, diagnostic smart objects, even personal mobile devices.

## Slide 19
For example, A smelting facility extracts metals from their ores. The facility uses both heat and chemicals to decompose the ore, leaving behind the base metal this is a multistage process and the data and controls are all accessed via various control rooms in a facility.
An RLTS utilizes small and easily deployed Wi-Fi RFID tags that attach to virtually any material and provide real-time location and status. IOT sensors allows components and materials on an assembly line to “talk” to the network. If each assembly line’s output is tracked in real time, decisions cab be made to speed up or slow production to meet targets, it id easy to determine how quickly employees are completing the various stages of production.

## Slide 21: Smart Connected Building
Buildings are beginning to deploy sensors throughout the building to detect occupancy. Motion detection occupancy sensors work great if everyone is moving around in a crowded room and can automatically shut the lights off when everyone has left, but what if a person in the room is out of the sight of sensor ? An unintelligent sensor on the wall that wants you to turn off the light.
Sensors are used to control heating, ventilation and air-conditioning(HVAC). Temperature sensors are spread throughout the building and are used to influence the building management system’s (BMS’s) control of air flow into the room.
Smart buildings are easier and cheaper to manage. When smart building sensors and occupancy detection are combined with the power of data analytics it becomes easier to demonstrate the floor plan usage and prove your case.

## Slide 22
The building automation system(BAS) has been deployed to provide a single management system for the HVAC, lighting, fire alarm, and detection system.
In early 2000s, Cisco and several other companies championed the convergence of voice and video onto single IP network that were shared with other IT applications.
The communication protocol responsible for building automation is known as BACnet(Building Automation and Control Network). BACnet defines a set of services that allow Ethernet-based communication between building devices such as HVAC, lighting, access control and fire detection systems.

## Slide 23
The digital ceiling is more than just a lighting control system. It encompasses several of the building’s different networks- including lighting, HVAC, blinds, CCTV and security systems and combines them into a single IP network.
Shift towards LEDs which offers low energy consumption and longer life.
The lower power requirements of LED fixtures allow them to run on power over Ethernet (PoE).
Figure 1-8 A Framework for the Digital Ceiling

## Slide 24
    In a digital ceiling environment, every luminaire or lighting fixture is directly network-attached, providing control and power over the same infrastructure.
    The transition to LED lighting means that a single converged network is now able to encompasses luminaries that are part of consolidated building management as well as elements managed by the IT network, supporting voice, video and other data applications.

## Slide 25
Modern LED Ceiling fixtures support occupancy sensors. These sensors provide high resolution Occupancy data collection, which can be used to turn the lights on and off.
The data can be combined with advanced data analytics to control other systems such as HVAC and security.
Modern lighting sensors integrate a variety of occupancy sensing-technologies, including Bluetooth low energy(BLE) and Wi-Fi. When someone walks near the light, the person’s location is detected, and the wireless system can send information to control the air flow from the HVAC system into that zone in real time, maximizing the comfort of the office worker.

## Slide 26: Smart Creatures
IoT provides the ability to connect living things to the internet. Sensors can be placed on animals and even insects. A well-known applications of IoT with respect to animals focuses on what is often referred to as the “connected cow”. Sparked, a Dutch company developed a sensor that is placed in a cow’s ear.
The sensor monitors various health aspects of the cow as well as its location and transmits the data wirelessly for analysis by the farmer.
The data from each of these sensors is approximately 200MB per year. Once the data is collected, a complete statistics on every cow is obtained. The following factors can be identified in cows:
Affecting herd as a whole and changes in diet.
Early detection of disease as cows tend to eat less days before they show symptoms.
Allow the detection of pregnancy in cows.

## Slide 27
Another application of IoT to organisms involve the placement of sensors on roaches.
Researchers at North Carolina State University are working with Madagascar hissing cockroaches in the hopes of helping emergency personal rescue survivors after a disaster.
An electronic backpack is attach to a roach. This backpack communicates with the roach through parts of the body. Low level electrical pulses to an antenna on one side makes the roach turn to the opposite side because it believes it is encountering an obstacle. The cerci of the roach are sensory organs on the abdomen that detect danger through changing air currents. When backpack stimulates the cerci, the roach moves forward because it thinks a predator is approaching.

## Slide 28
The electronic backpack uses wireless communication to a controller and can be “driven” remotely. Imagine a fleet of these roaches being used in a disaster scenario, such as searching for survivors in a collapsed building after earthquake.
The roaches are naturally designed to effectively move around objects in confined spaces. The use of roaches in this manner allows for the mapping spaces that rescue personnel cannot access, which helps search for survivors.
To help a person trapped in the rubble of a collapsed building, the electronic backpack is equipped with directional microphones that allow for the detection of certain sounds and the directions from which they are coming.
Software can analyze the sounds to ensure that they are from a person rather from a leaking pipe. Roaches can then be steered toward the sounds that may indicate people who are trapped. The microphones provide the ability for rescue personnel to listen in on whatever sounds are detected.

## Slide 29: Convergence of IT and OT
IT | OT
IT supports connections to the Internet along with related data and technology systems and is focused on the secure flow of data across an organization. | OT monitors and controls devices and processes on physical operational systems. These include assembly lines, utility distribution networks, production facilities, roadway systems.
IT organization is responsible for information systems of a business such as email, file and print services, databases. | OT is responsible for the devices and processes acting on industrial equipment, such as factory machines, meters, actuators, electrical distribution automation devices, SCADA(supervisory control and data acquisition).

## Slide 30: Table1.3: Comparing Operational Technology(OT) and Information Technology(IT)
Criterion | Industrial OT Network | Enterprise IT Network
Operational focus | Keep the business operating 24*7 | Manage the computers, data, and employee communication system in a secure way
Priorities | Availability Integrity Security | Security Integrity Availability
Types of data | Monitoring, control and supervisory data | Voice, video, transactional and bulk data
Security | Controlled physical access to devices | Devices and users authenticated to the network
Implication of failure | OT network disruption directly impacts business | Can be business impacting, depending on industry, but workarounds may be possible
Network upgrades | Only during operational maintenance windows | Often requires an outage window when workers are not onsite; impact can be mitigated
Security vulnerability | Low: OT networks are isolated and often use proprietary protocols | High: continual patching of hosts is required and the network is connected to Internet and requires vigilant protection.

## Slide 31: IoT Challenges
Challenge | Description
Scale | The scale of OT can be several orders of magnitude larger. E.g. one large electrical utility in Asia recently began deploying IPv6-based smart meters on its electrical grid. The number of meters in the service area is tens of millions.
Security | With more “things” becoming connected with other “things” and people, security is an increasingly complex issue for IoT. Your threat surface is now greatly expanded and if a device gets hacked, its connectivity is a major concern.
Privacy | As sensors become more prolific in our everyday lives, much of the data they gather will be specific to individuals and their activities. This data can range from health information to shopping patterns and transactions at a retail establishment.
Big data and Data analytics | IoT and its large number of sensors is going to trigger a deluge of data that must be handled. This data will provide critical information and insights if it can be processed in an efficient manner. The challenge is evaluating the massive amounts of data arriving from different sources in various forms and doing so in a timely manner.
Interoperability | Some of the protocols and architectures are based on proprietary elements and others are open. IoT standards are helping minimize this problem.